## Slide 1: Compiler Flow using Mflowgen
Deepak Gopalan

## Slide 2: Mflowgen Review - Basics
  Modular flow specification and build-system generator for ASIC and FPGA design-space exploration built around sandboxed and modular steps.
  Mflowgen allows you to programmatically define and parameterize a graph of steps (i.e., sandboxes that run anything you like) with well-defined inputs and outputs.
  Build system files (e.g., make, ninja) are then generated which shuttle files between steps before running them.
  Modularity – Reuse of steps
  Sandboxed – Self contained steps, well defined inputs and outputs

## Slide 3: Mflowgen Review – How to Set up
  Define the graph – define the steps, add them to the graph and define connections between the steps. Can connect steps automatically by name or explicitly connect certain outputs of one step to certain inputs of another step. These have to be specified in a python script (construct.py)
  Configure the Steps – specify the inputs, outputs and commands (how to go from inputs to outputs) Also can specify parameters, pre/post conditions for the step. Each step needs to have a directory which contains a configure.yml file where these details are entered
  Build the design by invoking mflowgen and then run the steps

## Slide 4: Mflowgen Review – Some cool Features
  Parametrization – useful for exploring design spaces within a single graph
  Parameter range is defined in the graph
  Multiple copies of the parametrized step are created, each for one value of the parameter
  Every step downstream the parameterized step also has different copies for each parameter value

## Slide 5: Mflowgen Review – Some cool Features
  Cloning – Instantiate the same step multiple times in one graph. The cloned steps are all similar, but they can be fed by different inputs
  Assertions – Pre and Post conditions
File class: to check if a file is present
to check the occurrences of certain string in a file
Tool class: to check if a tool required for the step is set up
Can define custom pytest assertions
Can have multiline assertions which call some python helper functions
  Stashing - share pre-built steps between people working on the same graph

## Slide 6: Compiler Flow
  Halide to Hardware
  PE Generation
  MetaMapper
  Clockwork
  RTL Simulation
  DC Synthesis
  Primetime PX

## Slide 7: Mflowgen Chart

## Slide 8: Halide to Hardware
  The Input to this step is the application specified in Halide
  Halide programs contain two parts: an algorithm and a schedule
  The algorithm specifies the computation output, while the schedule specifies the scope of the accelerator, memory hierarchy, which loops to parallelize, Loop tiling etc.
  The schedule allows the user to trade off locality, recomputation, and parallelism using different loop transformations

## Slide 9: Halide to Hardware
  The Halide program is then lowered to HalideIR
  computational kernels represented by statements enclosed in for-loops
  memory operations represented by reads and writes to multi-dimensional arrays.
  Next, the compiler lowers the application to CoreIR graph
  compute statements transformed into bitvector primitives (add, sub, mul)
  loop nests transformed into streaming memories called unified buffers
  Lowering the application from Halide to a CoreIR dataflow graph facilitates the subsequent mapping to hardware

## Slide 10: Halide to Hardware

## Slide 11: PE Generation step
  Takes application CoreIR as an input
  Identifies candidate PE architectures by performing frequent subgraph analysis
1) Identify all the frequent subgraphs from the CoreIR
  2) Find maximal independent set of each subgraph
  (check non-overlapping subgraph frequency)
  3) Merging subgraphs which share some operations

## Slide 12: PE Generation step
  The extent of merging can be tuned in order to move from multiple simple PEs to few but more complex PEs
  Generates rewrite rules for mapping CoreIR operations to PE – uses an SMT Solver
  Hardware generation – produces RTL Verilog for the PE
  Functional model of PE in python

## Slide 13: MetaMapper
  This step maps the CoreIR compute nodes to the PE by using the rewrite rules from PE generation step to perform instruction selection
  Gives the number of PEs used in the design, which can be used to tune PE Generation step

## Slide 14: Clockwork
  Takes MetaMapper’s output and performs memory mapping to map the abstract memories (unified buffers) with memory tiles
  From the memory hardware specified in lake, high-level specifications such as capacity, number of ports, port widths, read/write delays are extracted
  These specifications of hardware memory modules are used to produce a mapping of the application unified buffers to the hardware memory modules.
  Hardware independent and Hardware dependent stages

## Slide 15: Clockwork – Hardware Independent Rewrite
  Determine data-reuse using polyhedral analysis on the unified buffer’s access patterns
  Same data fetched multiple times – use registers to reduce memory bandwidth
  Obsolete data – overwrite it to reduce memory capacity

## Slide 16: Clockwork – Hardware Dependent Rewrite
  Transforms abstract memory to concrete hardware memory using extracted high-level hardware specifications
  Banking to increase bandwidth
  Chaining to increase capacity
  Vectorization to match interface width

## Slide 17: Experiments – Flowgraph

## Slide 18: Experiments – Gaussian – Freq. subgraphs from CoreIR

## Slide 19: Experiments – Gaussian – Subgraph 0
in0 * const0
in0 * in1
in1 >> in0
const0
in1 + in0

## Slide 20: Experiments – Gaussian – Subgraph 1
(in0 * const0) + in1
in0 * in1
Const0
in1 >> in0
in0 + in1

## Slide 21: Experiments – Gaussian – Subgraph 2
(in0 * in1) + in2
in0 * in1
Const0
in2 >> in1
in1 + in2

## Slide 22: Experiments – Gaussian – Subgraph 3
in2 + (in0 + in1)
in2 * in1
Const0
in0 + in1
in2 >> in1

## Slide 23: Experiments – Gaussian – Subgraph 0 + 1
(in0 * const0) + in1
in0 * const0
in0 * in1
Const0
in1 >> in0
in0 + in1

## Slide 24: Experiments – Gaussian – Subgraph 1 + 3
(in0 * const0) + in1
(in0 + in2) + in1
in0 * in1
in2 >> in1
in0 + in1
const0

## Slide 25: Experiments – Gaussian – Subgraph 0 + 1 + 2
(in0 * const0) + in1
in0 * const0
(in0 * in2) + in1
in0 * in2
in2 + in1
const0
in2 >> in1

## Slide 26: Experiments – Gaussian – Subgraph 0 + 1 + 2 + 3
(in0 * const0) + in1
in0 * const0
(in0 + in2) + in1
(in0 * in2) + in1
Const0
in0 + in1
in0 * in2
in2 >> in1

## Slide 27: Gaussian - Number of PEs Used
Subgraph | Number of PEs
0 | 21
1 | 14
2 | 22
3 | 26
0 + 1 | 13
1 + 3 | 14
0 + 1 + 2 | 13
0 + 1 + 2 + 3 | 13

## Slide 28: Gaussian – Area – old, wrong flattening
Subgraph | Comb | Buf | Non Comb | Total
0 | 7329 | 3514 | 44421 | 51751
1 | 8047 | 3924 | 44421 | 52469
2 | 8255 | 4000 | 44421 | 52677
3 | 8896 | 4545 | 44421 | 53318
0 + 1 | 6021 | 2297 | 44421 | 50443
1 + 3 | 7883 | 3803 | 44421 | 52304
0 + 1 + 2 | 7027 | 2893 | 44421 | 51448
0 + 1 + 2 + 3 | 7442 | 3285 | 44421 | 51864

## Slide 29: Gaussian - Power (mW) – old, wrong flattening
Subgraph | Sw | Int | Leak | Total
0 | 1.8 | 24.4 | 1.0 | 27.1
1 | 2.3 | 25.2 | 1.0 | 28.5
2 | 2.5 | 25.3 | 1.0 | 28.9
3 | 2.2 | 25.1 | 1.1 | 28.4
0 + 1 | 1.58 | 24.0 | 0.9 | 26.5
1 + 3 | 2.3 | 25.0 | 1.0 | 28.3
0 + 1 + 2 | 2 | 24.3 | 1.0 | 27.3
0 + 1 + 2 + 3 | 2.1 | 24.5 | 1.0 | 27.6

## Slide 30: Gaussian – Area - New
Subgraph | Comb | Buf | Non Comb | Total
0 | 29971 | 1637 | 44459 | 74430
1 | 20503 | 1054 | 44459 | 64962
2 | 31237 | 1483 | 44457 | 75694
3 | 37804 | 1924 | 44460 | 82264
0 + 1 | 19009 | 982 | 44459 | 63468
1 + 3 | 21725 | 1074 | 44421 | 66186
0 + 1 + 2 | 19073 | 973 | 44461 | 63534
0 + 1 + 2 + 3 | 20193 | 994 | 44461 | 64655

## Slide 31: Gaussian - Power (mW) - New
Subgraph | Sw | Int | Leak | Total
0 | 4.2 | 25.2 | 1.5 | 31.0
1 | 2.0 | 23.6 | 1.3 | 26.9
2 | 1.8 | 23.6 | 1.5 | 26.9
3 | 3.3 | 24.7 | 1.6 | 29.6
0 + 1 | 2.0 | 23.6 | 1.2 | 26.8
1 + 3 | 1.8 | 23.4 | 1.3 | 26.5
0 + 1 + 2 | 1.7 | 23.4 | 1.2 | 26.3
0 + 1 + 2 + 3 | 1.7 | 23.4 | 1.3 | 26.4

## Slide 32: Some stuff to add on
  Use activity factors for power numbers – testbench for RTL simulation available for app mapped to lassen PE (uses random input data), which produces SAIF report to be passed onto DC and PTPX. Need to modify testbench generator for custom created PE.
  Check other apps
  Complete flow to Place and Route